## Slide 1: MOSSEVEIEN PORTAL
Bane NOR
(Railway Administration of
Norway)
Bane NOR
(Railway Administration of
Norway)
Railway construction
Keller Grundbau
Guglgasse 15, BT4a / 3. OG 1110 Wien Austria
Over 1 million EURO
The project
  The Follobanen project is currently the largest infrastructure project in Norway. The project includes 22 km of new railway from Oslo to Ski. The main part of the works was the construction of a Portal from the transition zone from Drill and Blast to the Cut and Cover tunneling into Oslo S.
The challenge
  Reduction of water permeability and reinforcement of weakness zone directly affecting the excavation of the tunnel through the transitional zone.
  Lack of space due to rural surrounding area with roads in use and railway traffic.
The solution
  With its large foundation portfolio, Keller has been able to assist the client with specialized injection technologies. Due to the difficult soil conditions many different types of machinery and drilling techniques were utilized to ensure the stabilization of the overburden soil before the grouting works. The first step was the installation of a temporary casing and cleaning of the hole in order to penetrate in the faults of the weakness zone. Afterwards grouting from bottom to the top in 5 meter stages with packers was executed. If the required GIN parameters were not fullfilled, redrilling of the hole was necessary and injections with different mixtures and parameters applied.
Injections
Double Head Drilling
Single Head Drilling
357 points with 4096m of injection drillings up to 38m depth
Grouting container with 6 pumps and automatic monitoring system of the parameters, over 120.000 liters injected
Use of GIN Method with different mixtures certified with Lugeon testing
Application
Method
Market
Client
Main contractor
Contract Value
Permeation Grouting
with GIN method
Key points
oslo s, norway
Contracting project manager
Anne Marie Syvertsen Anne.Marie.Syvertsen@banenor.no
Project start date: February 2017
Project end date: September 2017